| Nr. | Descriere | Cantitate |
| --- | --- | --- |
| 1 | Caracteristici minime Fujitsu Primergy RX230M5: Chassis: Rack mount, 1U, 8 x 2.5-inch drives chassis Processor: Two (2x) Intel Xeon Silver 4210, 2.2 GHz base frequency, 10 cores, Hyper-Threading Technology, Virtualization Technology (VT-x) Memory: min. 64 GB DDR4 ECC Registered Memory RAID controller: Hardware RAID 0/1/10/5/6 Controller, min 2 GB Flash-Backed Write Cache, Hard drives: Two (2x) 1TB SATA 12Gbps Hot-Plug; Two (3x) 960GB SSD Mixed-use Hot-Plug; Cooling system: Full Redundant hot plug fans Power supply: Dual, Hot-Plug, Redundant power supplies, Platinum, or equivalent, Certified Network interfaces: Four (4x) – 1 GbE One (1x) – 1 Ethernet Management port Diagnostic LEDs: On front panel Server management (SM): Dedicated Ethernet NIC for management. Local and remote control of system resources (manage, diagnose and monitor). Remote power control, remote firmware updating, remote presence, virtual media attachment to a server of USB drive, CD/DVD drive Serial over LAN, DHCP, IPMI V2.0, CIM, SNMP, email alerts LDAP user authentication Browser based administration with full control over the remote host server's display, keyboard, and mouse, including host OS graphical interface. Virtual media option that provides virtual CD drive and remote image mounting. Rack mounting rails: Rack mount kit Cables (per unitate): Two (2x) Power cables, PDU connection, Warranty, service, support, and upgrades: 3-Year Next Business Day (Manufacturer problem diagnosis and Support, Replacement parts and materials, Onsite hardware support, Firmware updates, Software support) Condiții de livrare: Ofertantul câștigător (Vânzătorul) se obligă să livreze bunurile în decurs de 10 zile calendaristice după intrarea în vigoare a contractului. | 2 |