CAIET DE SARCINI

| Item No. | Description / Specification of Goods |
| --- | --- |
|  | Network attached storage |
|  | Type | NAS |
|  | Form Factor | Rack 2U, 3U, 4 or 5U rackmount include Rack kit which Cable Management Arm |
|  | Memory installed | min. 64GB |
|  | Maximum support memory | up to 128GB |
|  | Memory slot | 4x UDIMM |
|  | USB ports | min. 2x USB 3.2 Gen 1 min. 2x USB 3.2 Gen 2 |
|  | PCIe Slot | min. 4x (PCIe Gen 3) |
|  | Storage capacity | min.12x 12TB SATA min.6 GB/s min.7.2k rpm 3.5" |
|  | Supported drive bay | up to 16x drive 3.5" |
|  | Hot-swappable | Yes |
|  | Storage Manager | create RAID, configuration a logical unit number, monitoring the storage usage, inspect drives etc. |
|  | Supported protocols | IPv4 and IPv6 CIFS, AFP, FTP, NFS, WebDAV, iSCSI, Telnet, SSH, SNMP, VPN, possibility created a domain controller |
|  | Supported disk type | min: RAID 0, RAID 1, RAID 5, RAID 6, RAID 10 |
|  | Power Supply | 2x Power Supplies, min. 400W, 100-240V AC, 50/60Hz |
|  | Connectivity LAN | min. 2x 10 Gb/s ports SFP+, 4x 1Gb/s |
|  | Extra cable | 2x 10 Gb/s ports SFP+, 2 Meters |
|  | Warranty | min. 3 years official manufacturer warranty |